## Slide 1: Unit 4. Coding and Capacity on Fading Channels
Ece-gy 6023. Wireless communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe symbol mapping for QAM constellations
Implement symbol detection for faded symbols
  Compute average BER and SER on AWGN and flat channels and compare
Identify if a system can be model as slow or fast fading
For slow fading, compute outage probability and capacity under a fading model
For fast fading, compute the ergodic capacity
Create a TX and RX chain for flat and fading channels with given components
  Symbol equalization, soft symbol detection, interleaving, channel decoder
Use MATLAB tools for common channel encoders and decoders
  Convolutional, turbo codes and LDPC codes

## Slide 3: Outline
Uncoded Modulation over Fading Channels
Outage Probability and Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels

## Slide 4: Uncoded Modulation
Symbol mapping
TX bits
TX filter
Fading channel
Symbol demodulation
RX filter
This section: Uncoded modulation over fading channels
  That is, communication with no channel encoding and decoding
We will show uncoded modulation works very poorly
Virtually all practical wireless systems use coding of some form
QAM symbols
RX QAM symbols
RX bits

## Slide 5: Mathematical Model
Symbol mapping
TX bits
Fading channel
Symbol demodulation
Simple memoryless model:
  and TX and RX QAM symbols
  : Fading channel gain, Noise
Assumptions:
  Perfect synchronization
  No ISI in the channel (or the equalizer has removed the effect of the ISI, more on this later)
  We can look at one symbol at a time
RX QAM symbols
RX bits
TX QAM symbols

## Slide 6: Review: Bit to Symbol Mapping
= sequence of bits.
= sequence of complex symbols
  Each symbol has one of possible values
Modulation rate: bits per symbol
  Each bits gets mapped to one symbol
Symbol period: One symbol every seconds.
Bit rate of bits per second
T
Ex. with M=4 symbols =2 bits per symbol

## Slide 7: Review: QAM Modulation
QAM: Most common bit to symbol mapping in wireless system
  bits mapped to and bits mapped to Q
  Each dimension is mapped uniformly
bits/sym
bits/sym
bits/sym
QPSK

## Slide 8: ML Estimation for Symbol Demodulation
Consider single symbol:
  Drop the sample index
  is a QAM symbol
Maximum likelihood estimation:
Given and :
Hence,

## Slide 9: Equalization and Nearest Symbol Detection
Likelihood:
MLE is:
Here, = equalized symbol.
Procedure:
  Step 1: Equalize the symbol:
  Step 2: Find closest to in the complex plane

## Slide 10: Decision Regions
ML estimate is closest point in constellation to :
Decision region for a point :
  set of points where is the closest point:
Decision region for s1
s1 (closest point)
s2
s3
s4
Example: Decision region in QPSK

## Slide 11: Error Probabilities on an AWGN Channel
Error probabilities:
  Symbol error rate, SER: Prob symbol is misdetected
  Bit error rate, BER: Probability of a bit is in error
  Assume TX symbols are uniformly distributed
First consider AWGN model:
  No fading
SER for QPSK can be shown to be:
  SNR =
z
w
No error
z in correct decision region
Error
z not in correct decision region
sm
sm
w
z

## Slide 12: SER for AWGN Modulation
Error formula can be derived for most QAM mappings
  See, e.g., Proakis
For an AWGN channel:
  SER typically decays exponentially with SNR
  Ex: for QPSK

## Slide 13: Ex: BER Simulation for 16-QAM
See demo
Easy to do in MATLAB

## Slide 14: SNR on a Fading Channel
Now return to a fading channel:
Equalization:
  Effective noise after equalization
SNR after equalization:
  Noise energy after equalization:
  SNR is
  SNR varies with the fading
Average SNR is:
High SNR
Low SNR
SNR:

## Slide 15: Average SER on a Fading Channel
Fading channel:
With fading, SNR is random ,. SNR is
Define the average SER:
  A function of the average SER
  Represents the average over independent channel realizations
If is Rayleigh distributed, is exponential with

## Slide 16: Example: SER on QPSK with Rayleigh Fading
Rayleigh fading: is exponential
QPSK: for large
Lemma: Suppose that is exponential
  Detailed proof below. Write
Average SER: From Lemma
Average SER decays as
In AWGN channel, SER decays as
Much slower decay

## Slide 17: Comparison of Fading vs. AWGN
Error rate with fading is dramatically higher.
Ex. for QPSK:
  No fading, SER decays exponentially
  With fading, SER decays with inverse SNR
Similar relations for most other constellations
Need much higher SNR
SER with QPSK
No fading
Rayleigh fading

## Slide 18: 16-QAM Example
See demo
Large gap between AWGN and Rayleigh

## Slide 19: Lemma for Average of Q function
Lemma: Suppose that is exponential .
Proof:
  Change order of integral

## Slide 20: In-Class Exercise

## Slide 21: Outline
Uncoded Modulation over Fading Channels
Outage Probability and Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels

## Slide 22: Coding Over Fading Channels
Lesson from previous section:
  With fading, uncoded modulation cannot provided sufficient reliability
  Error rate decays slowly with SNR
Channel coding:
  Send data in blocks
  Block contains redundancy
  If some parts fade, can still recover block
All commercial wireless systems use coding!

## Slide 23: Slow Fading vs. Fast Fading
To analyze coding over a fading channel, consider two extreme cases
Slow fading
  Block length , channel coherence time
  All symbols in block are faded equally
  Entire packet sees same SNR
  Performance measured by outage probability and outage capacity
Fast fading
  Block length
  Symbols in packet see many realizations of channel
  Performance measured by ergodic capacity

## Slide 24: Slow Fading and Outage Probability
Coding block sees an SNR
SNR varies but is constant over each block
  Transmission time Coherence time
Code has some target SNR
  Target could be based on some block error probability
Assume has some distribution
Outage probability:
  The fraction of time target is not met
  Can be computed from the distribution of
SNR
Time
Coding block

## Slide 25: Outage Probability for Rayleigh Fading
Suppose a channel is Rayleigh fading
SNR is exponentially distributed with some mean
Outage probability:
Average SNR for a given outage probability:
Fade margin: Additional SNR needed above target for a given outage probability:
  In linear scale:
  In dB:

## Slide 26: Fade Margin Example
Example:
  Target SNR is dB
  Outage probability:
From previous slide, necessary average SNR is: dB
The average SNR needs to be 20 dB above target!
Plot: Fade margin vs. outage
Fade margins with Rayleigh fading can be enormous!
Max fade
20 dB fade margin
Fade=0

## Slide 27: Outage Capacity
Suppose we can achieve some rate as a function of SNR
When SNR is random, so is the rate
Outage capacity: Rate, we can achieve with a probability
Example:
  Suppose system has 20 MHz bandwidth and the rate is 60% of Shannon capacity
  The average SNR is 20 dB.
  What is the outage capacity for 1% outage assuming Rayleigh fading?
Solution:
  From earlier, for Rayleigh fading, the SNR achievable at the outage probability is
  In linear scale,
  Outage capacity: Mbps
  At the average SNR the rate is Mbps

## Slide 28: System Implications for Outage
With slow Rayleigh fading, need to add large fade margin
Channel coding does not mitigate fading
  Fading causes all bits to fail
  Still may be useful to use channel coding (e.g., for noise across the symbols)
Possible solutions?
  If there is motion, perhaps we can retransmit later
  Go to a lower rate (needs less SNR)
  Just accept that some locations are in outage
Some of these solutions are discussed in the next unit

## Slide 29: Fast Fading Model
Coding block much longer than coherence time
Simple information theoretic model
  Channel gains are i.i.d. with some distribution
  and
  Each symbol experiences an SNR
  Blocklength
Assumption implicitly assumes:
  We have a very long blocklength
  Can experience many independent fades
SNR
Time
Coding block

## Slide 30: Ergodic Capacity
Fast fading model:
  Channel gains are i.i.d. with some distribution
Ergodic capacity: Theoretical maximum rate per symbol
  Assume average transmit power limit
  Maximum taken over all codes and blocklength
  No computational limits
Theorem: Ergodic capacity of a fast fading channel is:
  Value is in bits per symbol
  Expectation is over channel distribution
SNR
Time
Coding block

## Slide 31: Shannon Ergodic Capacity Key Remarks
From previous slide, ergodic capacity is:
Theoretical result: Needs infinite computation and delay
  We will look at performance of real codes next
TX does not need to know channel
  But RX must estimate and use this channel.
  We will see RX design is critical
If TX knew the channel, it could get theoretically get slightly higher rate
  Uses a method called water-filling
  Place more power on symbols with better SNR.
  Gain is not typically large and rarely used in practical wireless systems
SNR
Time
Coding block

## Slide 32: Comparing Ergodic and Flat Capacity
Fading capacity is always lower than flat fading
  Keeping the same average SNR the same
  This fact follows from Jensen’s inequality:
But gap is not that large at low to moderate SNRs
  See graph to the right. Loss of only 1-2 dB in
Conclusions:
  We should try to code over large number of fading realizations
  In this case, the capacity loss is theoretically small
  Much better than the case of uncoded modulation
We will look at practical codes next

## Slide 33: In-Class Exercise
Indoor environment
Look at large scale and small-scale fading

## Slide 34: Outline
Uncoded Modulation over Fading Channels
Outage Probability and Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels

## Slide 35: Coded Communication on an AWGN Channel
Channel coding
Symbol mapping
Channel with noise
Soft symbol demodulation
Channel decoder
Info bits
Coded bits
Info bits
LLR
We first review channel coding on a flat channel:
TX symbols
RX symbols

## Slide 36: Uncoded vs. Coded Modulation
Uncoded Modulation:
  Modulate raw information bits
  One symbol at a time.
  Any symbol is in error, data packet is lost!
Coded modulation:
  Transmit in blocks (also called frames)
  Add extra parity bits to each block for reliability
  Decode entire block together
Info bits
Symbol mapping
Complex symbols
Info bits block
Coding
Info
Parity
Coded bit block
Block of symbols
Symbol mapping

## Slide 37: Key Parameters of Block Codes
An block code has:
  = number of information bits (input block size)
  = number of coded bits (output block size)
  = number of additional bits, typically parity
  = coding rate = .
Typical values in wireless:
  Block size: to 10000
  Code rate: to
k information bits
“message”
k info bits
n-k parity
“Bit Codeword” : n coded bits
Coding

## Slide 38: Coded Communication on an AWGN Channel
Channel coding
Symbol mapping
Channel with noise
Soft symbol demodulation
Channel decoder
Info bits
Coded bits
Info bits
LLR
We first review channel coding on a flat channel:
TX symbols
RX symbols

## Slide 39: Soft Symbol Demodulation
Set-up: Coded bits get mapped to symbol
  Receive
Uncoded systems use hard decision detection:
  Estimate bits from symbol
  Makes a discrete decision.
Coded systems generally use soft decision demodulation:
  Output log likelihood ratios:
  positive more likely
  negative more likely
Soft demod
Symbol mapping
+

## Slide 40: LLR for QPSK
TX symbol:
RX symbol:
LLR for bit
  [Each dim has
  Likelihood:
  With some algebra:
01
11
10
00
Mapping of bits

## Slide 41: QPSK LLR Visualized
LLR for is:
LLR for is:
Mapping of bits
more likely
more likely

## Slide 42: High Order Constellations
Higher order constellations (eg. 16- or 64-QAM)
Each constellation is a point is a function of multiple bits.
Example: For 16-QAM
  In phase dimension depends on bits
Cannot compute LLR on an individual bit directly
Two bits:
00
01
11
10
Mapping of bits

## Slide 43: High Order Constellations
To create LLRs for individual bits use total probability rule:
Resulting bitwise LLR:
Two bits:

## Slide 44: High Order Constellations
LLRs can have irregular shapes
Not simple linear function as in BPSK / QPSK case
Often use approximations
More info: Caire, Taricco and Biglieri, “Bit-Interleaved Coded Modulation," 1998.
Two bits:
LLR for c2 LLR for c1

## Slide 45: Coded Communication on an AWGN Channel
Channel coding
Symbol mapping
Channel with noise
Soft symbol demodulation
Channel decoder
Info bits
Coded bits
Info bits
LLR
We first review channel coding on a flat channel:
TX symbols
RX symbols

## Slide 46: Maximum Likelihood Channel Decoding
Channel coding: Information block: generates a codeword
Receiver gets a vector number of complex modulation symbols
Channel decoder: Goal is to estimate (or equivalently ) from .
Ideally will use maximum likelihood decoding:
  Finds the codeword that is most likely given the receive vector
Channel coding
Symbol mapping
Channel with noise
Demod
Channel decoder
Info bits
Coded bits
Info bits
LLR
TX symbols
RX symbols

## Slide 47: Decoding via the LLRs, Part 1
Channel decoding: Ideally select codeword to maximize
Equivalently we can maximize:
  Highest likelihood relative to the all zero codeword
Assume likelihood factors as:
  is the complex modulation symbol containing coded bit
Hence, objective is:

## Slide 48: Decoding via the LLRs, Part 2
From previous slide
But since or :
Hence, the channel decoder can find the codeword by maximizing:

## Slide 49: Decoding Complexity
Channel decoding ideally selects codeword
Brute force optimization is exponentially difficult:
  Suppose the information block is
  Each generates one codeword
  Optimization must, ideally, search over possible codewords
  Computationally impossible
Coding design requires searching over coding mechanisms with:
  Computationally tractable decoding
  But still have good performance

## Slide 50: Quest for the Shannon Limit
Shannon capacity formula and random codes, 1948.
  Determines the capacity, but no practical code to achieve it.
Hamming (7,4) code, 1950
Reed-Solomon codes based on polynomials over finite fields, 1960
  Used in Voyager program, 1977. CD players, 1982.
Convolutional codes.
  Viterbi algorithm, 1969. Widely used in cellular systems. (Viterbi later invents CDMA and founds Qualcomm)
  Typically, within 3-4 dB of capacity
Turbo codes, Berrou, Glavieux, Thitimajshima, 1993.
  Able to achieve capacity within a fraction of dB.
  Adopted as standard in all 4G and 5G cellular systems by the late 1990s.
LDPC codes
  Similar iterative technique as turbo codes. Re-discovered in 1996.
  Used in 5G systems

## Slide 51: Convolutional Codes
Encode data through parallel binary (usu. FIR) filters
Example convolutional code:
  Rate = ½ (two output bits (for each input bit .
  Constraint length K=3 (size of shift register)
  Additions are modulo two
Benefits:
  Easy to implement, good performance
  Can be decoded with Viterbi algorithm Iterative procedure similar to dynamic programming procedure
  See digital comm class for more details
b[t]
c1[t]
c2[t]
z-1
z-1
z-1

## Slide 52: Convolutional Code Performance
Convolutional codes performance:
  > 5 dB better than uncoded BPSK at low BER
Only moderate constraint length (K=7) needed
Source: Proakis, “Digital communications”

## Slide 53: Simulation in MATLAB
MATLAB has excellent tools
  Conv encoder / decoder
  LLR
See demo
Rate=1/2, QPSK, K=7 conv code

## Slide 54: Turbo Codes
Turbo codes:
  Concatenation of two convolutional codes Typically IIR and short (K=3)
  Interleaver: Randomly permutes the input bits
Output
  Input bit, and
  Parity bits from each convolutional encoder
  With no puncturing R=1/3
Discovered in 1993, ,
  Berrou, Glavieux, Thitimajshima, 1993.
  Able to achieve capacity within a fraction of dB.
Used in 3G and 4G standards

## Slide 55: Turbo Code Iterative Decoding
Turbo decoder uses an iterative message passing
  Decode each convolutional coder one at a time
  Use posterior information of one code as prior for the other
Good performance in small number (usu. ~8) iterations
  Typically use short codes (K=3).
  Complexity similar to convolutional codes
Close to Shannon capacity
  Much better than convolution codes
Source: Lin, Costello, “Error Control Coding”

## Slide 56: LDPC Codes
Code defined by a bipartite graph
  Connects coded bits and parity bits
  Data information bits
Also use a message passing decoder
  Based on graphical models
Obtains excellent performance
  Lower complexity than turbo decoder
  Good for very high data rate applications
Used in 802.11ad and 5G New Radio
LDPC Graph
Coded bits
Parity check bits

## Slide 57: In-Class Problem
Simulate the commercial 5G NR LDPC code
  A rate 1/3 code
  Much better performance than convolutional code

## Slide 58: Outline
Uncoded Modulation over Fading Channels
Outage Probability and Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels

## Slide 59: Coded Communication on a Fading Channel
Fading channel
Info bits
Info bits
Now consider fading channel:
To handle fading we need to introduce a few new blocks
  Interleaving and de-interleaving
  Equalization
Inter-leaver
Symbol mapping
Channel encoder
Equal-ization
De-inter-leaver
Channel decoder
New blocks
New block

## Slide 60: Symbol Equalization via Inversion
Received noisy symbol:
Symbol equalization:
  Estimate from
  Also obtain a noise estimate (needed for LLR)
Channel inversion:
  Symbol estimate
  Noise estimate:
Symbol Equalization
+

## Slide 61: MMSE Symbol Equalization
Received noisy symbol:
MMSE estimation:
  Use linear estimate
  Select to minimize
Resulting estimate (shown with simple algebra):
  Estimate:
  Noise variance:
Provides lower noise estimate than channel inversion
Symbol Equalization
+

## Slide 62: Interleaving and De-Interleaving
Problem: Fading is correlated in time
  Will result in many consecutive faded bits
  Many codes perform poorly if errors are together
Interleaver
  Shuffles the bits before symbol mapping
  De-interleaving is performed on LLRs
  Randomizes locations of errors
  Removes time correlations
Many interleavers used in practice
  Random interleaver (with some seed at TX and RX)
  Row-column interleavers…
Inter-leaver
De-Interleaving

## Slide 63: Simulation
Simulation:
  Convolutional code, rate with QPSK
  Constraint length
  Plotted is block error rate (BLER) vs.
Gap between AWGN and fading:
  Approximately 4 dB at BLER =
  Much smaller gap than uncoded modulation

## Slide 64: Simulating in MATLAB
Transmitter and Channel Fading
Channel Noise and Receiver

## Slide 65: Summary
Fading: Causes variations in SNR
Uncoded modulation:
  Dramatically increases error rate
  Must add significant fade margin
Coding with slow fading
  All symbols are faded together
  Fade margin still necessary
Coding with fast fading
  Can greatly mitigate fading
  Recover faded bits with redundancy
  But needs to encoded over many independent fades
  Transmit over many coherence or bandwidth