## Slide 1: Unit 5. Adaptive Modulation and Coding
Ece-gy 6023. Wireless communications
Prof. Sundeep rangan

## Slide 2: Questions
Fading causes variations in SNR
  Large scale and small-scale variations
TX must adapt the MCS
Basic questions:
  How does the TX know the MCS to select?
  How does it send the selected MCS to the RX?
  What happens if it selects the MCS incorrectly?
High rate
Low rate

## Slide 3: Learning Objectives
Describe ARQ protocol in 802.11 WiFi systems
Implement and analyze a simple trial-and-error MCS selection system
Describe the key components in scheduling in 5G NR
  Data and control channels, timeline
Compute delays and packet ordering with errors in a multiple ARQ processes
Describe the CSI-RS channel
Implement and simulate simple CSI measurements from the CSI-RS measurements
Describe and analyze Hybrid ARQ
Implement and simulate a simulate multi-process HARQ process over a fading channel

## Slide 4: Outline
MCS Selection and ARQ in 802.11 Wireless LAN
MCS Selection, Scheduling and ARQ in 5G NR
CSI Feedback and Link Adaptation in 5G NR
Hybrid ARQ

## Slide 5: 802.11 Family of Wireless LAN Standards
Full details on Wikipedia

## Slide 6: MCS Selection in 802.11
Each packet is transmitted in some MCS
Ex: 802.11n (see full table on Wikipedia)
  Eight possible MCS options
  Up to four possible spatial streams (More on this in MIMO)
Trade off SNR requirement with data rate
MCS Options in 802.11n (HT) and 802.11ac (VHT)

## Slide 7: Sending the MCS Selection
Data
Training
Signal
FCS
Training field: To detect presence of packet, synchronize RX and train equalizer
Signal field: Packet format including MCS and PDU length
Data: User data plus MAC information such as address info
FCS: Frame check sum to detect if data is received correctly
Fixed MCS
Variable MCS
MCS selection

## Slide 8: Example Details in 802.11n
Packet components:
  L-STF and HT-LTF1: Training fields for synchronization and equalization training
  HT-SIG: Encodes the MCS and PDU length
  Data: The PDU encoded at the MCS
From http://rfmw.em.keysight.com/wireless/helpfiles/n7617/Content/Main/MIMO_OFDM_Signal_Structure.htm

## Slide 9: Example: MCS Selection on a Fading Channel
Simple simulation:
  3 path channel
  Doppler spread 10 Hz
  Narrowband fading
  Avg SNR = 15 dB
  Time is divided into 1ms time slots
At each time slot:
  Select MCS based on SNR
  Observe discrete rate options
See demo

## Slide 10: Packet Errors
Each MCS will have a required SNR
Packet will experience an SNR
If Packet may be received with errors
Two questions:
  How does the RX detect the errors?
  What can the TX do?
Packet fails
Packet passes
SNR target

## Slide 11: Detecting Errors with CRCs
How does the receiver know that a data packet received successfully?
Each packet contains a CRC (cyclic redundancy check)
  CRC = f(payload)
Receiver checks if CRC=f(payload) for decoded packet
If CRC fails, receiver knows there is an error
If CRC passes, very high probability that packet is correct
  Chance that CRC passes for a random packet is 2-n, n = num bits in CRC
P = Payload
(Up to 1000s of bits)
CRC=f(P)
Typ. 16 to 32 bits
P = Payload’
CRC’
Checks if CRC’ = f(P’)
Received packet
Transmitted packet

## Slide 12: Auto-Repeat Request (ARQ)
Can overcome errors with multiple attempts
  After each attempt RX replies
  ACK if data received successfully and NAK if data fails.
  RX success can be checked with a CRC on packet (later)
  TX resends on NAK.
Data
NAK
NAK
Attempt 1
Attempt 2
ACK
Attempt 3
Fade level
Data
Data

## Slide 13: Error Probability with ARQ
Let
  SNR in attempt (assume flat fading for now)
  minimum SNR to pass
Assume independent fades in each transmission
Probability of failure after trials:
  Decreases exponentially
  No loss: with infinite attempts, every packet passes eventually
Essentially exploits time diversity

## Slide 14: Problems with ARQ
Delay
  Time between transmissions coherence time
  Example: Hz.
  Say we separate transmissions by sec.
  Four transmissions takes > 400 ms.
Still need a reasonable estimate of SNR
  Suppose average SNR is
  Select an MCS with some minimum SNR
  If we target MCS with High probability of error, many wasted attempts
  If we target MCS with Under-utilize the channel

## Slide 15: Trial and Error Rate Adaptation
How do we set MCS in absence of channel state information?
Typically use simple “trial and error” method:
  No ACK => Try lower rate for retransmission
  ACK => Occasionally try higher rate.
  “Probe” to see if channel has improved
Does not require any channel quality feedback.
Widely used in 802.11 transmitters
Channel SNR
Min SNR for attempted MCS
NAK
NAK
ACK
NAK
ACK
Dec MCS
Dec MCS
Inc MCS
Drop MCS

## Slide 16: Decoding Time in 802.11
In 802.11 systems, ACK is sent very rapidly
ACK sent within Short Interframe Space
  Typically, around 10 us
  Very challenging engineering effort
Start decoding the packet while it is being received
  Cannot interleave across OFDM symbols
RX packet
Conv decoding
ACK
SIFS time

## Slide 17: In-Class Problem

## Slide 18: Outline
MCS Selection and ARQ in 802.11 Wireless LAN
MCS Selection, Scheduling and ARQ in 5G NR
CSI Feedback and Link Adaptation in 5G NR
Hybrid ARQ

## Slide 19: Scheduling in Cellular OFDM Systems
Transmissions are scheduled by the base station
Each assignment from the base station contains:
  A UE identity
  Direction (uplink or downlink)
  Time and frequency resources for data
  MCS for the data
  Time and frequency resources for the ACK
  Other formatting information
Scheduling with OFDM enables:
  Very flexible resource allocation among multiple users
  Rapid adaptation to channel conditions and traffic requirements
  Used in 4G LTE and 5G NR
Time
Frequency
Assignment
Data
ACK
UE1
UE2

## Slide 20: Resource Blocks in 5G NR
Assignments are in units of resource blocks
  One slot in time = 14 OFDM symbols (normal mode)
  12 sub-carriers in frequency
Each assignment has one or more RBs in a slot
Slot time depends on sub-carrier spacing
1 slot = 14 OFDM symbols
12 subcarriers

## Slide 21: Key Channels in 5G NR Data
Downlink: gNB to UE
PDSCH: Physical downlink shared channel
  DL data
PDCCH: Physical downlink control channel:
  Assignments for both the uplink and downlink
  Schedules resources on PDSCH and PUSCH
Uplink: UE to gNB
PUSCH: Physical uplink shared channel
  UL data
  May also contain UL ACKs
PUCCH: Physical uplink control channel:
  Scheduling requests
  UL ACKs (if PUSCH is not available)

## Slide 22: PDCCH Scheduling
UL and DL grants sent on PDCCH
  DCI: Downlink control information
  Many different DCI formats
All DCI contain
  Time allocation: Slot number
  Frequency allocation: Set of RBs
  MCS
  ARQ location (DL grant only)
  Many other formatting details…

## Slide 23: 5G NR MCS Options
Transport block (TB):
  Transmission associated with one assignment
  Occurs in one or more RBs in a slot
Each TB is transmitted with some MCS
  Modulation and coding scheme
  Currently there are 28 options
Set by the base station depending on SNR

## Slide 24: Example: Computing TB Size
Suppose that in a system with a slot size =125 s, a downlink grant:
  Spans 10 RBs
  Uses MCS 12 (16-QAM, Code rate =434/1024)
  On average 10 REs in each RB are used for overhead (e.g., PDCCH, reference signals, …)
What is the transport block size and instantaneous data rate?
Solution:
  Each RB has 12 x 14=168 total REs.
  There are 168-10=158 for data
  The TB size will be: bits
  The instantaneous data rate is Mbps

## Slide 25: Downlink Scheduling Timeline
ACKs for downlink data transmitted on PUCCH
  Physical uplink control channel
  Can also be transmitted on the uplink data channel if it is available
PDCCH assignment
PDSCH data
ACK/NACK on PUCCH
Decode attempt
Scheduling decision
Initial TX
Next TX or Re-TX
DL data
DL data
Decode attempt

## Slide 26: Uplink Scheduling Timeline
In uplink, UE must inform gNB it has data to be transmitted
  Can use scheduling request (SR) or buffer status report (BSR)
No explicit ACK needs to be transmitted
  gNB can grant the re-transmission or not
UL grant on PDCCH
PDSCH data
Data on PUSCH
Decode attempt &
re-schedule
UL data
UL data
SR on PUCCH
Scheduling decision
UL grant on PDCCH
Data on PUSCH
New or Re-TX
Decode attempt &
re-schedule

## Slide 27: PDCCH Channel Configuration
5G NR provides very flexible allocation of resources to the PDCCH
  Allocated to control resource sets (CORESETs)
  CORESETs provide possible locations of the PDCCH assignments
  UEs search CORESETs for PDCCH allocated to it
Configurability can tradeoff delay, overhead, …
See MATLAB excellent 5G Toolbox video, PDCCH mapping to Coreset, for all the details

## Slide 28: Multiple HARQ Processes
Transmissions involves several delays:
  Transmission & decode of data
  Transmission & decode of ACK
  Decision for scheduling
To enable continuous transmissions:
  Use multiple HARQ processes in parallel
  5G NR supports up to 16
HARQ process scheduling
  HARQ processes indicated in DCI
  Can be in any order
  Very flexible
Decode time
ACK decode & schedule time
HARQ Process
1
1
2
3
4
2

## Slide 29: In-Class Exercise

## Slide 30: Outline
MCS Selection and ARQ in 802.11 Wireless LAN
MCS Selection, Scheduling and ARQ in 5G NR
CSI Feedback and Link Adaptation in 5G NR
Hybrid ARQ

## Slide 31: CQI Feedback
Trial and error rate adaptation is inexact
  Fading can result in many wasted attempts
Ideally, TX needs to needs to know the channel quality information (CQI)
In cellular systems, CQI is often performed via feedback
  CQI is measured at the UE
  Fed back to the base station in a CQI report
Periodic CQI reports (typ. ~100 per sec)
Data with rate based on CSI

## Slide 32: CSI Feedback in NR DL
gNB sends periodic CSI RS:
  CSI reference signals
  Typically, 1 CSI-RS per 5 to 10ms
UE measures CSI from the CSI-RS
Sends back report to the gNB
gNB can correctly select MCS
CSI RS
CSI Report
Assignment w/ MCS
Data
Measures CSI
Selects MCS
gNB
UE

## Slide 33: CSI-RS Configuration in MATLAB
Ex to the right:
  One zero power (ZP) CSI-RS: Can measure noise
  One non-zero power (NZP): Can measure signal strength
Configurable structure
  Periodicity
  Density
  Position in RB
Trades off CSI estimation accuracy and overhead

## Slide 34: Visualizing the CSI-RS Configuration
Example to the right:
  Two CSI-RS configurations sent
  CSI-RS0: Zero power
  CSI-RS1: Non-zero power
  1 slot = 1 subframe = 1 ms
  15 kHz sub-carrier spacing
Pattern repeats over RBs
Sent once every 10 ms
Total CSI-RS overhead in this case:
1 ms

## Slide 35: Estimating the CSI using ZP and NZP
On ZP CSI-RS:
  There was no transmitted signal
  Receive noise on the signal
  Noise estimate
On NZP CSI-RS:
  Receive
  TX symbol, channel gain
  Average power:
  SNR on that RE:
  Estimate SNR on that symbol:

## Slide 36: Example Simulation
Three path channel, average SNR = 10 dB
Simulated in frequency-domain
Significant frequency selective fading
  Bandwidth
  But coherence time 1ms.
SNR [dB] per RE

## Slide 37: Example Estimate
Plotted:
  True channel on symbol for the CSI-RS
  Red: Estimates on the CSI-RS sub-carriers
Individual CSI-RS estimates are noisy
But averaged values can be accurate

## Slide 38: Estimate the CSI with NZP CSI-RS Only
Often can estimate CSI with NZP CSI-RS only
Suppose channel is approximately constant over REs used by CSI-RS
Then we can model received symbols on the REs as:
  Channel gain
  known TX symbol,
Using linear estimation, we can estimate channel and noise in the group
  Factor is to eliminate bias in variance estimate
Estimate for the SNR on group:
  Subtract to remove noise on the transmitted signal dimension.

## Slide 39: Implementation in MATLAB
Typically perform average in one RB
  Assuming channel is roughly constant over this bandwidth
  Depends on coherence bandwidth
For each RB get:
  Noise estimate and channel estimate
Compute wideband SNR estimate:
  average of in RBs
  average of in RBs
See demo

## Slide 40: Uplink Power Control
Uplink is power controlled (more on this later)
  Keep transmit RX power at a target
  Save UE battery, reduces interference
  Minimizes dynamic range and near-far effect in multi-user systems
Cannot use RX SNR as a measure of channel quality
Reference signals (PUCCH, SRS, …)
Gain control
Fast power control
Power amplifier (PA)
Measure SNR

## Slide 41: Uplink CSI
Suppose SNR is measured on some reference signal,
  Can be sounding reference signal (SRS), PUCCH, PUSCH, …
UE periodically sends a power headroom (PAH),
  Difference between maximum available power and current reference signal powr
Then, maximum SNR can be computed from
Provides basis for scheduling the UE
Max RX power
Max TX power
PA headroom
Ref signal TX power
Thermal noise
Ref SNR
Ref signal RX power
Max SNR

## Slide 42: Effect on CSI Error
In general, there will be errors in the CSI at the TX:
  The RX does not measure the CSI exactly
  Time delay between the CSI report and TX based on the CSI
To quantify effect, let = SNR
  Model as a random variable
  Randomness quantifies the

## Slide 43: Analysis
Let SNR experienced on transmission
  Assume is constant over coding block
  SNR is i.i.d. across different blocks,
Link-rate model: Let rate achievable if we knew the rate.
  Ex:
If the TX knew the SNR, the average rate we would get is:
If the TX does not know the SNR and selects a target SNR, it should maximize:

## Slide 44: Further Topics
The 5G NR standard provides many powerful features for CSI reporting
  Flexible configuration of the CSI-RS and CSI reporting
  Rich CSI reporting: wideband, per sub-band, multiple layers, …
Optimizing the use of the CSI-RS is a complex and interesting design problem
  Channel quality estimation algorithms
  Tradeoffs in overhead and accuracy
  Channel quality tracking and prediction
  Particularly challenging when we get to multi-antenna systems

## Slide 45: In Class Exercise: CSI Tracking

## Slide 46: Outline
MCS Selection and ARQ in 802.11 Wireless LAN
MCS Selection, Scheduling and ARQ in 5G NR
CSI Feedback and Link Adaptation in 5G NR
Hybrid ARQ

## Slide 47: Hybrid ARQ
Standard ARQ wastes transmissions on losses
  No data sent in each failed transmission
Hybrid ARQ concept:
  On each failure, store received symbols
  Combine new symbols with old until successfully decoded
“Failed” transmissions are not wasted
Two methods:
  Chase combining
  Incremental redundancy

## Slide 48: Combing Multiple Symbols
SNR with combining is the sum of the individual SNRs
Suppose we receive the same symbol times:
SNR on each transmission is:
Use match filter to estimate :
  Signal energy =
  Noise energy =
  SNR after combining:

## Slide 49: Combing Symbols Using LLRs
Combining across symbols can be done by adding LLRs
Suppose we receive the same symbol times:
Say some coded bit appears in this symbol
The LLR using all symbols is:
Assuming independence of noise in difference symbols:
We can simply add the LLRs obtained from transmissions

## Slide 50: HARQ Chase Combining
Transmit symbols in each attempt
RX computes the LLRs for the block
Adds to previous LLRs
Continues to add LLRs until decoder passes
TX
RX
Attempt 1
LLRs
Decoder
NACK
Attempt 2
Decoder
ACK
Add LLRs

## Slide 51: Analysis
Let SNR experienced on transmission
  Assume SNR is constant over coding block
  Model as a stationary random process
Link-rate model:
  Let rate achievable if the TX knew the SNR
  Ex:
Hence, if the TX knows the SNR:
  Average rate
Time slot
SNR

## Slide 52: Rate Analysis with Chase HARQ
Suppose in time slot , TX selects a rate with minimum SNR
No HARQ:
  If packet passes, link will get rate
  Packet will pass with probability
  Average rate:
Chase combining HARQ:
  Let First slot index that packet passes
  If , rate is
  Hence, average rate with Chase combining:
  Observe since

## Slide 53: Delay-Accuracy Considerations
Suppose that is constant. SNR in each transmission is
Will terminate after transmissions when:
Worst case delay:
Worst case SNR error:
Delay-accuracy tradeoff: With larger delay , received SNR matches the required SNR better

## Slide 54: Rateless Gaussian Random Code
Chase combining effectively creates a repetition code
  Not optimal
Alternate method: “infinite” random code:
  information bits, messages
  Each code word is an infinite iid sequence
If we take first symbols where is large, we get
  Code that is optimal for AWGN or fading channel
  Code can be reliably received if ,
  avg capacity per symbol.

## Slide 55: Using a Rateless Code
Suppose capacity not known
Terminate when
Can achieve arbitrarily close to capacity without knowing anything!
  Works for fading or constant channels
info bits
symbols each TX

## Slide 56: IR Illustrated
TX1
Decode w/ part 1
LLR buffer
NAK
TX2
Decode w/ parts 1 and 2
ACK
Mother code
Decode 1:
  Use part 1
  Treat parts 2, 3 as erasures
Decode 2:
  Use parts 1,2
  Treat part 3 as erasure
TX
RX

## Slide 57: Practical Rateless Codes
Incremental redundancy
  Code data with low rate “mother code” (Usually rate 1/3 or 1/5)
  In first TX send systematic bits + some parity
  Decoder treats missing bits as erasures.
  If fail, TX sends more parity bits
  Continue until it passes
In 3GPP codes, each TX is called a redundancy version
First proposed by Mandelbaum 1974
Hamidi-Sepeh et al, Analysis of 5G LDPC Codes Rate-matching Design, 2018

## Slide 58: 5G NR HARQ Performance
Simulation with QPSK
With multiple transmissions:
  Can obtain reasonable over wide range of SNRs
  Staircase throughput curve
Selecting wrong MCS may not lead to poor rate:
Ex: At SNR=1 dB
  Get ~0.95 bps/Hz with option 1 (QPSK, rate=0.95)
  Get ~1 bps/Hz with option 1 (QPSK, rate=0.5)
Hamidi-Sepeh et al, Analysis of 5G LDPC Codes Rate-matching Design, 2018
Passes in 1 TX
4 TX
3 TX
2 TX

## Slide 59: Analysis
Exact analysis complex
  Depends on puncturing and precise fading pattern
  Must use simulation
Effective SNR per bit
  Computes an “effective SNR”
  Accounts for fading and HARQ
  Many simulations show this model predicts actual performance on real codes well
  Used widely in network simulations to avoid simulating the LDPC codes

## Slide 60: Effective SNR Per Bit
Shannon capacity after transmissions
  SNR on symbol
  = number of complex symbols per transmission
  total symbols
Effective SNR per bit: Value of such that
  = number of information bits
  If constant, then that would be experienced
Key result: For most practical codes:
  Performance on a fading channel Performance on a constant channel with

## Slide 61: Comparison to Chase Combining
Chase combining: Energy accumulation
IR: Mutual information accumulation
IR is always better than Chase combing:

## Slide 62: Practical Considerations
Cellular standards use very powerful coding methods
Provides excellent performance
But presents several implementation challenges
Often need very large LLR buffer
  Must be stored on chip
  LLR memory often larger than decoder or even the entire modem!
Decoding delay:
  Typical turnaround time is several slots (100s of us to milliseconds)
  Much longer than WiFi (Recall SIFS time is 10 us)